## Slide 1: Developing the Conceptual Model
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Definition
A simplified representation of a real aquifer system including the hydrogeologic units, boundaries, sources, and sinks

## Slide 3: Conceptual Model

## Slide 4: Grid-Based Numerical Model

## Slide 5: Sample Conceptual Model
Notes: http://www.epnrm.sa.gov.au/Water/Groundwater.aspx

## Slide 6: Sample Conceptual Model
Notes: http://md.water.usgs.gov/publications/fs-150-99/html/index.htm

## Slide 7: Alternate Conceptual Models
Notes: http://crustal.usgs.gov/projects/Handcart_Gulch/watershed.html

## Slide 8: Parsimony
Keep the model complex enough to be useful, but simple enough to be manageable
“Everything should be made as simple as possible. But not simpler.”
– Albert Einstein

## Slide 9: Characterize Aquifer Units
Determine principal hydrogeologic units
Hydrogeologic Unit
A zone that exhibits common hydraulic properties
May include multiple geologic units

## Slide 10: Hydrogeologic Units

## Slide 11: Hydrogeologic Units

## Slide 12: 2D vs. 3D?
Is the flow primarily horizontal?
Is it necessary to capture the vertical component of flow in light of the modeling objectives?
Regional vs. local model?
How much data is available?

## Slide 13: 2D Areal Models
Single layer models
Used when flow is primarily horizontal

## Slide 14: 2D Profile Models
Used when flow field is constant along a horizontal axis

## Slide 15: Full 3D Models
Full 3D equations are solved for each point in the model
Used when vertical component of flow is important to modeling objectives

## Slide 16: Steady State vs. Transient
How significant are the transient stresses?
How close are the stresses to the critical parts of the model?
Is sufficient transient data available?
1991
1992
1993

## Slide 17: Boundary Conditions
How far should the model be extended?
No-Flow
  Physical barrier (e.g. bedrock outcropping)
  Groundwater divide
  Parallel flow boundary
Head
  Constant head (strong source/sink)
  Head dependent (river, drain, lake)

## Slide 18: Sources and Sinks
What are the main sources and sinks you want to include in the model?
Rivers
Drains
Lakes,
Reservoirs, Springs
Wells
etc.

## Slide 19: Water Budget
Determine a water budget for the site in question
Includes an estimate of the total inflows and outflows
Notes: http://ess.nrcan.gc.ca/2002_2006/gwp/p3/a9/index_e.php

## Slide 20: Water Budget