## Slide 1: Hydraulic Head Concepts
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Pore Pressure
u = pore water pressure
u = h2*gw
gw = g*r
  g = gravity
  r = density of water

## Slide 3: Heads, Pressures, & Flow
Example 1
Does flow occur from a to b?

## Slide 4: Heads, Pressures, & Flow
Example 2
Does flow occur from a to b?

## Slide 5: Bernoulli's Equation
What work is done in moving a unit mass of fluid from pt. A to pt. B?

## Slide 6: Work, pt. 1
Work done in lifting mass from A to B:
W1 = (weight)(distance)
= (mg)z
= (1*g)z
= gz

## Slide 7: Work, pt. 2
Work done changing kinetic energy
W2 = (1/2)mvb2 - (1/2)mva2
= (1/2)1vb2 - (1/2)1va2
= (vb2 - va2)/2

## Slide 8: Work, pt. 3
Work done in compressing fluid isothermally
W3 = D(PV)
= DP(V) + DV(P)
= DP(V) + 0(P)
= (ub – ua)(m/rw)
= (ub – ua)/rw

## Slide 9: Total Work
Total work
f = W1 + W2 + W3
f = gz + (vb2 - va2)/2 + (ub – ua)/rw
f = total potential
Divide by g to get potential in terms of weight (not mass):
f/g = z + (vb2 - va2)/(2g) + (ub – ua)/gw
f/g = total head = Dhab

## Slide 10: Bernoulli’s Equation
Dhab = z + (vb2 - va2)/(2g) + (ub – ua)/gw
where
z = zb – za
Therefore
Dhab = (zb – za) + (vb2 - va2)/(2g) + (ub – ua)/gw
Dhab = (zb + vb2/(2g) + ub/gw) - (za + va2/(2g) + ua/gw)

## Slide 11: Bernoulli’s Equation
Can be written in terms of total head at a particular point:
h = z + v2/(2g) + u/gw
htotal = hel + hvel + hp

## Slide 12: Elevation Head (hel)
hel
datum
Consistent datum must be used
= distance above some arbitrary datum

## Slide 13: Velocity Head (hvel)
v (ft/sec) | v2/2g
1 X 10-6 | 1.6 X 10-14
1 X 10-4 | 1.6 X 10-10
1 X 10-2 | 1.6 X 10-6
1 X 100 | 1.6 X 10-2
Therefore, we generally neglect velocity head
Typical values for gw problems:
= v2/2g

## Slide 14: Pressure Head (hp)
= u/gw

## Slide 15: Bernoulli’s Equation for GW
Typically written as:
h = z + u/gw
where h = Level to which water would rise in a piezometer inserted at the point in question. Measured relative to some arbitrary datum.

## Slide 16: Example
Since hb = ha, no flow
Flow only occurs when there is a change or difference in total head

## Slide 17: Example 1 - Revisited
hp(a) = hp(b)
hel(a) > hel(b)
h(a) > h(b)
Therefore water flows from a to b
(see class exercise)

## Slide 18: Example 2 - Revisited
Since ha > hb, flow occurs from a to b